## Slide 1: Interactive Sculpture with Garbage PCs
Paul Davies
xraylab.org

## Slide 2
Notes: Bandwidth – Paul Davies
Bandwidth is an interactive installation that attempts to explore the issue of information poverty. Information is becoming increasingly important and concrete in our society and culture. Those that cannot access and manipulate information technology are forming a new lower class. There are many factors that contribute to not being able to access information: monetary poverty, educational poverty, sensory and physical poverty. These people have not been invited to the information-centric future. Bandwidth addresses the challenges of these subcultures, using one of the most pronounced examples of information poverty; the sensory poverty of blindness. The visually impaired are one group that are prime candidates to join the ranks of the information poor, because the bulk of information is communicated via visual media.
Until recently, access to information has been guided with the intention of equal access. Access to the telephone or television networks is provided at a fixed cost to all individuals at an equal tariff regardless of geographical remoteness. This principle will not be part of our increasingly information-centric society. Services will only be provided to those with the resources needed to obtain them.
Bandwidth is the difference between the upper and lower frequency of a signal, which is directly proportional to the rate at which information can be transmitted. In the dialect of computer culture, it has come to mean simply the latter: the rate at which one can access transmitted information. More generally, however, mere access to information is not enough; to be useful, one must be able to access the information that is personally relevant, and in a timely fashion.
The point of this installation is simple: some people have no bandwidth. The visually impaired are at a distinct disadvantage in a society that communicates visually. The primary tool for the manipulation of information within the present societal context is the computer. At this time, the use of a computer in anything but a trivial way requires the sense of sight. Without sight, one immediately becomes information-poor.
Bandwidth consists of a computer monitor and a braille pad, which are both controlled by a simple (286) computer. The braille pad has six metal pins that form braille letters that a user experiences through the palm of her hand. Information is displayed simultaneously on the monitor and the pad. Although the computer can transmit any type of information, the braille pad can only display text. Although no information is destroyed, the information transmitted to the pad is rendered useless: the bandwidth is so narrow that reading text with the pad is virtually

## Slide 3
Notes: Bandwidth Detail – Paul Davies

## Slide 4
Notes: Opaque Detail – Paul Davies
Opaque plays with our trust in the encoding of digital information. We invest considerable trust in objects like magnetic strips on credit cards and bar codes on products. Is that trust so well founded? As in our general experience, Opaque is trustworthy most of the time and faithfully encodes a visitors name as a bar coded nametag. However, a significant number of barcodes are not trust worthy. The interactions between visitors with ‘good’ nametags and those with ‘flawed’ nametags are often amusing.
Opaque consists of barcode generating software, a grocery store barcode scanner and an electronic pixel sign. The software encodes people's names to barcodes - sometimes with error. Using the generated barcode, a name label is printed. Users can then scan the printed nametag to display on the pixel board

## Slide 5
Notes: Opaque – Paul Davies

## Slide 6
Notes: Skins (2001) - Doug Back
Mirror, lights, TV, computer, electronics (Qbasic program) * The audio output from a VCR (tuned to a local TV station) is fed into a LM3915 chip which contains 10 comparators. Three of these outputs are attached to the P.Port inputs. Six of the P.Port outputs go to Solid State Relays and control the six small spot lights. The computer in the Skins installation "watches" a live TV channel and attempts to map the emotional content of the program onto the viewer's face. The viewer sits in a chair watching their face in a mirror. Arranged around the mirror are six small, computer controlled spot lights. They can create 'dramatic lighting effects' on the face of the viewer in this small theatre. A TV sits near their feet, the sound is set to a low familiar murmur that permeates the gallery. The audio from the TV program is fed into a very simple, hand made Analog to Digital Converter. This breaks the sound down into four outputs Silent, Low, Medium and Loud. The computer program notes the audio level and more importantly measures both the length of a discrete sound and length of silence in between the sound events. The program passes this data through a number of software filters. These filters attempt to discern the current emotional state of whatever is on the TV.
A few simple examples: _If the recent sounds have been Low to Medium, very long in length with very short pauses in between then it assumes music is playing. _If the sounds are Loud, of very short length with very short pauses in between the computer assumes there is a fight taking place or someone is shouting. _ If it thinks some one is talking it carefully watches the pauses between sentence, only people of great importance are allowed long poinient silences between utterances, every one else must pack as much information as possible into their allotted time. I wrote a lot of these filters, each filter is influenced by the emotional tone preceding it. The derived emotional state is then used to turn on a pattern of spot lights. The six lights provide sixty_four possible lighting effects to be shone on to the viewers face. If the computer thinks the emotional content is "bad" then the lights under the face tend to get excited. If the computer thinks the TV is playing something "good" then the viewers face is lite using the lights above the face. I'm not an especially great programmer. I just wrote filters until the program started reacting to the TV in ways I couldn't explain and then I stopped. It doesn't like opera and considers several actors annunciations to be evil. The piece does however illustrate the frequency with which our emotions are meant to be tugged and does keep the viewer somewhat in_character during its performance.

## Slide 7
Notes: Jacob Wrestling with the Angel (1985) Doug Back - (Qbasic program) Wooden platform, videotape, VCR, monitor, flowers, clock, old clothes, electronics, twenty dollar bill, computer, motor * When the recording for this piece gets made, a tone generator (555 chip) encodes audio pulses onto the video tape, when ever I want the camera to move (when ever I push a button). One of the P.Port inputs "listens" for the tone and moves the camera with a stepper motor. The stepper motor is controlled by the P.Port. An Optical Encoder on the motor (fed back into the P.Port inputs) allows the computer to count steps... keeping track of the cameras position. On play-back the computer listens for tones on the video tape and the program pulses the stepper motor (and watches the Optical Encoder) to make sure that cameras movement is synchronised to the objects that appear on the video monitor. A 10' by 10' wooden platform is raised 2' off the floor. A set of stairs allow the audience to walk on the platform. In the centre of the platform, a hole has been cut out so that the viewer can see a motorized surveillance camera and some of the area under the platform. The camera pans back and forth, and appears to stop and look at objects under the platform. A television monitor is placed close to the observation hole. The motor that turns the camera is synchronized to the video tape by sound tones, an electronic circuit and a computer program, so that when the camera is pointed at an object... the object appears on the TV screen. However the camera is not turned on. What appears on the screen is pre-recorded. A clock under the platform is keeping 'real time', flowers, leaves, ice and other natural materials wilt and melt over the period of the exhibition. After a period of time it becomes apparent to the viewer that things are out of temporal sync. This piece is always site specific and the tape usually ends with a short recorded performance by the artist, under the platform.

## Slide 8
Notes: Jacob Wrestling with the Angel – Doug Back

## Slide 9
Notes: " Sect", (exterior and interior views) Doug Back 1996 (Qbasic program) * The joystick port is connected to a light cell and stares out the window of the gallery. This samples the average available light and tries to figure out the "time of day". Two P/Port outputs pulse the DC motors to perform the punching. The aggression of the punching (length of On pulses) depends on the "time of day". A one foot tall sculpture with motorized arms is programmed to preform a ritualistic movement. The movements are programmed to be something in between animal behaviour or a person shadow boxing. A projection system is built behind the sculpture so that a ten foot tall shadow of it is rear_projected onto the front window of the gallery. A single light cell is pointed out onto the street. The computer can read changes in light levels outside the gallery. _ 'Sect is a model that simulates, (through rudimentary artificial life), some low order brain function. The piece depends on an ambivalence as to what this function is. _ The gallery contains the mechanism for the projection and is responsible for its magnification to a frightening scale. _ The projection can't be seen during the day. _ The projection mechanism is inaccessible after the gallery has closed. _ I have attempted to emulate an "inner" and "outer" world, both of which are not separate but fully dependent on each other. _ I have attempted neuter the gender of the sculpture. (Ha!) 'Sect has been programmed with a strong tendency towards nocturnal behaviour. It has a light sensor to sample the ambient light levels in the outside world. As it gets darker, and as more of "us" go to sleep and dream, the more active it becomes. 'Sect has a very short memory of past light levels, but sufficient to be startled by sudden bright lights. When startled it freezes motion, a standard survival tactic, used by both predators and prey in their need to be less noticed, but now, totally useless when a car hurls towards them at night on a highway. Although there are many ways to simulate animal behaviour, I have chosen pseudo random numbers. I say pseudo because computers cannot generate true random numbers. In this instance 'Sect will repeat it's movements after 64 million iterations. These numbers are used to time the electronic impulses to its "muscles". I have attempted to tailor the numbers so that the movements do not look purely predatory, defensive and/or merely playful. 'Sect's light sensor is used to influence the urgency of these impulses. The numbers have been orchestrated to simulate movements that are not easily categorize as human or insect. Asking a dancer or a child to move like an insect or act in a predatory manner will always give you good results. Explaining to a machine how long to hold out its arm, how long to leave it there and how long to keep it held in so that it conveys human, insect, aggressive or playful qualities has been very instructional. As always I program computers to learn more about nature.

## Slide 10
Notes: "Wasp#" (2001) Doug Back (Visual Basic program) * Two P.Port outputs are hooked up to a Linear Stepper Motor. This moves the 'stage' back and forth. Two P.Port inputs are connected to limit switches... to rest the piece on start up and to know when the viewer has seen the all the wasps. They also 'rewind' the stage when the viewer reaches the end of the stage. Two P.Port inputs watch the switches in the joystick, for viewer control of the stepper. As the computer 'knows' the position of the stepper... it 'knows' what the viewer is looking at. The Visual Basic program plays audio files when the viewer is looking at particular objects. A microscope is mounted on a table over a motorized platform which the viewer moves back and forth with a joystick. Glued onto the platform are a number of dead wasps with accompanying texts, gleaned from warning labels on household products and garbage pick up from off the street. When the viewer looks into the microscope their left ear is in close proximity to a small speaker. The computer whispers information into the views ear as the objects move under the microscope. The viewer is supplied "teaser" information about each wasp; it's name, number, occupation, hints about the geographic location that they died in. By E-mailing the artist a return E-mail comes back with a story about the wasp they selected.

## Slide 11
Notes: Wasp # (detail) - Doug Back

## Slide 12: Why use a PC?
Availability / Cost
Usefulness
Ease of use / Programming / Start-up
Performance / Speed
Alternatives: Basic Stamp, Mac w/ Max

## Slide 13: Getting Free PCs
basement
thrift / goodwill / salvation army
used PC stores

## Slide 14: Interfacing a PC
Printer port
  digital input / output
Game port
  interrupt driven digital input
  pseudo analog input
Serial port
  universal, simple communications

## Slide 15: Software Environment
DOS
  Create bootable floppy from any DOS or Win 3.x / 9.x machine
  Useful: format.com, fdisk.exe
QBasic
  qbasic.exe, qbasic.hlp
BIOS
  booting without a keyboard

## Slide 16: Using the Printer Port – Pin out
Ground is on pins 18-25

## Slide 17: Printer Port - Output
Address &0378 (hex) or &0278 on second card
Bit | Pin | TTL level for “One”
0 | 2 | High
1 | 3 | High
2 | 4 | High
3 | 5 | High
4 | 6 | High
5 | 7 | High
6 | 8 | High
7 | 9 | High

## Slide 18: Using the output – sample circuit

## Slide 19: Printer Port - Input
Address &037B (hex) or &027B on second card
Bit | Pin | TTL level for “One”
0 | Unused | 
1 | Unused | 
2 | Unused | 
3 | 15 | High
4 | 13 | High
5 | 12 | High
6 | 10 | High
7 | 11 | Low

## Slide 20: Using the Printer Port - Software
Using QBasic
Output
  OUT &0378, n
  n is a bit field corresponding to pins 2-9 of the port
Input
  INP &037B, n
  n is a bit field (bits 3-7) corresponding to pins 10-13,15 of the port
  bit 7, pin 11 is inverted
Bit Fields
1 = 00000001
2 = 00000010
4 = 00000100
8 = 00001000
16 = 00010000
32 = 00100000
64 = 01000000
128 = 10000000
3 = 00000011
37 = 00100101
255 = 11111111
etc

## Slide 22: Example of using the Printer Port
Bandwidth

## Slide 23: Using the Game Port
Pong controller / Joystick

## Slide 24: Game Port – Joystick Circuit (analog)

## Slide 25: Game Port – Joystick Circuit (buttons)

## Slide 26: Using the Game Port - Software
Using QBasic
Buttons
  ON STRIG(n) GOSUB foo
  n is 0,2,4,or 8 and corresponds to switches on pins 2,7,10 and 14
  foo is a sub routine that is called when the button is pressed
Analog
  x = STICK(n)
  x is assigned the value from the pot (0-255)
  n is 0,1,2 or 3 and corresponds to pots attached to pins 1,8,9 and 15

## Slide 27: Example of using the Game port
Sect by Doug Back using a light cell

## Slide 28: Using the Serial Port
Common use of serial in many devices
Other computers, controllers, etc
Many ‘devices’ such as pixel display

## Slide 29: Serial Port Software
QBasic
Opening a COM port OPEN "COM1:19200,E,7,1,ASC,CD0,CS0,DS0" FOR INPUT AS #1 OPEN "COM2:4800,E,7,1,ASC,CD0,CS0,DS0" FOR OUTPUT AS #2
Reading from a port LINE INPUT #1, inpstr where inpstr is the text read from the port
Writing to a port PRINT #2, outstr where outstr is the string to be sent to the port

## Slide 30: Example of using the Serial Port
Pixel display
Bar Code Scanner

## Slide 31: Useful Books and References
Parallel Port Complete: Programming, Interfacing & Using the PC'S Parallel Printer Port by Jan Axelson, Janet Louise Axelson
Interfacing to the IBM Personal Computer by Lewis C. Eggebrecht
Many different books on QBasic

## Slide 32: Useful Books and References (cont)
http://www.lvr.com/parport.htm
http://www.doc.ic.ac.uk/~ih/doc/par/
Art and Robotics Group mailing list: http://interaccess.org/arg/arg-list.html

## Slide 33: Getting this presentation
www.xraylab.org
pdavies@xraylab.org